## Slide 1: EPICS V4 Expands Support to Physics Application, Data Acsuisition, and Data Analysis
L. Dalesio, Gabriele Carcassi, Martin Richard Kraimer, Nikolay Malitsky, Guobao Shen, Michael Davidsaver, BNL, Upton, Long Island, New York, U.S.A, Ralph Lange,Bessy, Berlin, Germany, Matej Sekoranja, Cosylab, Ljubljana, Slovenia, James Rowland, Diamond Light Source, Oxfordshire, England, Greg White, SLAC, Menlo Park, California, U.S.A. Timo Korhonen, PSI, Villigen, Switzerland.
ICALREPCS
October 14, 2011

## Slide 2: Outline
Version 3 recap
Version 4
High Level Application Architecture
Normative Data Types
Conclusions

## Slide 3: Version 3 – took 6 years to release
Started at GTA project in 1985 at LANL as a tool set used to develop a space based accelerator ;)
  Developed core: channel access and process database
  along with some three display managers: SNL, save/restore, archive, bumpless reboot.
In 1989 a collaboration started with APS.
  several other labs showed interest to collaborate.
EPICS release V3, shows up in 1991
  process database rewritten to clarify the interface to hardware and new record types.
  Channel access continues to mature.
10% of the original code became part of this release.
  This project developed three user interfaces to start the tradition

## Slide 4: Version 3 Supports Instrumentation
Records represented either an input signal, an output signal or an operation to perform on a set of signals
  Analog input, analog output, (multi-bit)binary input, (multi-bit) binary output, motor, event, PID, calc, etc…..
  Agreeing on what a device is – is difficult. Is it a power supply or a magnet? Does a motor have an LVDT, an encoder, back lash?
Records implement continuous control in an autonomous controller to perform DCS functionality.
Many different types of research and industrial facilities successfully applied this to their plant for equipment control.
Process Variables (PVs) are available across the network
  Any field of any record can be a process variable.
  Functions on PVs are: get, put, monitor
  This service was designed and implemented to be robust and fast (15K PVs per second to a client on a 100 MB network)
  Channels always have a time stamp, alarm severity, and alarm status – the simple data type was not useful in most cases
  Channels have metadata to describe display, control, and alarm information.
MANY clients were developed on this interface in many languages on many operating systems implementing the full range of SCADA capabilities.
  With two site developing EPICS, there were two display managers.

## Slide 5: Version 3 Has Limited Support for Devices
Records did not operate on things more complex than scalar signals.
  No time domain, no frequency domain, no images.
  No way to represent things more complicated than scalar signals and 1 dimensional arrays
Process Variables available across the network could not support everything needed
  No atomic command / response mechanism
  No way to ask for a PV subject to parameters.
  PVs metadata did not always fit properly for every field of a record – such as the display precision – what is the time stamp of this?
  Typically a get is done on connection for display, alarm limits, and control metadata changes are not reflected.
  Meta data was sent all of the time, so only time stamp and current alarm information is monitored.
MANY clients added layers on top of V3 Process Variables to implement more complex data models

## Slide 6: EPICS Version 3 Architecture
Distributed Front-Ends
MMLT, SDDS, XAL, SAD, CDEV, SPEC, GDA, etc…
Physical Device
Ethernet
EDM/MEDM/ DM2K/EDM/QT/IDL/ CSS
CAC
CAC
Other GUI tools
CAC
Diag Database
CAS
Physical Device
PS Database
CAS
Physical Device
RF Database
CAS
Physical Device
Vac Database
CAS
Physical Device
Util Database
CAS
C, C++, java, Matlab, SDDS, Python
CAC
Channel Archiver
CAC

## Slide 7: Version 4 is in Year 6 of Development
Started at Marty’s home in 2006 as a tool set used to develop a device based control.
  Developed core: PVData and Java IOC to support the creation of devices.
Later in 2006, Cosylab was contracted to develop PVAccess
  Transport PVData
  Provide all of the V3 communication along with command/response and others
  Perform as well as Channel Access V3 on version 3 types.
  Optimizes the transport by only sending the elements that have changed.
In 2009 several laboratories showed interest in developing services in this environment
V4 alpha release shows up in 2011
  The team is much smaller
50% of the original code became part of the release
  More efficient since we are not developing user interfaces

## Slide 8: Version 4 Supports Complex Data Structures
Java IOC can represent devices
  We will likely not implement devices, as it is still difficult to agree on what these are
  We will use V3 records at NSLS II.
PVData (PVs) are available across the network
  Functions on PVs are: get, put, monitor, put/process/get (command/response)
  It is also hard to create object models on more complex devices such as a telescope or an accelerator.
Normative types are defined to provide metadata for more complex constructs: multi-channel array, table, N dimensional Array, Image.
  PVData always has a time stamp, alarm severity, and alarm status
  Vectors have useful metadata and distinctions: time domain vector, frequency domain vector, histogram
  Operations can be performed on two PVs with the same normative types.
PVService supports creating middle layers services
MANY servers are being developed on this interface to implement middle layer services for accelerator control and data acquisition.

## Slide 9
Specific Normative Data Types
NTMultichannelArray – represent a collection of single values as an ordered array
e.g. all of the temperatures along a beam line or the Australian Synch’s Concatenate Record used on AI’s
NTTimeDomainArray
e.g. a scope trace from a digitizer or the Circular Buffer in the Compress Record
NTHistogram e.g. information on a 60 Hz power supply RB posted every hour or the Histogram in the Compress Record
NTNDArray e.g. multiple frames of a detector taken at 1 KHz for 1 second
NTFrequencyDomainArray
e.g. FFT of 10 KHz data taken for 1 second to study noise frequencies or FFT record output
NTStatistic e.g. any data being compressed from its original rate – fast sampling in hardware to EPICS DB,
new function on any database waveform, response from a request to an archive server
NTImage e.g. image data being collected at a detector into the areaDetactor application
NTTable e.g. a way to return any list of values or collection of name, value pairs of different data type such as twiss parameters
or the metadata for a camera set up: filter, exposure time, camera used, etc…
This is the catch all data type that can define a structure of single values or arrays (of the same length)
NTChannelFinderDirectory
e.g. returned as an ordered list of PVs from a query to a directory service to populate a multi-channel array or table

## Slide 10: SLAC RDB Server Done Last Night
Example : Get modelled Twiss parameters (and other stuff) of all devices, sorted by Z greg% getRdb modelTwiss:Extant.FullMachine structure ResultSet string normativeType NTTable double[] ORDINAL [0.00000,1.00000,2.00000,7.00000,9.00000,…] string[] ELEMENT_NAME [CATHODE,DBMARK80,BEGIN_OF_CATHODE TO BXG,SOL1,SOL1,…] string[] EPICS_CHANNEL_ACCESS_NAME [CATH:IN20:111, , ,SOLN:IN20:121,SOLN:IN20:121,XCOR:IN20:121…] double[] Z_POSITION [2014.70,2014.70,2014.70,2014.80,2014.90,…] string[] POSITION_INDEX [BEGIN,BEGIN,BEGIN,BEGIN,MIDDLE,…] double[] LEFF [0.00000,0.00000,0.00000,0.200000,0.200000, …] double[] TOTAL_ENERGY [0.00600000,0.00600000,0.00600000,0.00600000,0.00600000,0.00600000,…] double[] PSI_X [0.00000,0.00000,0.00000,0.00445946,0.00949753,…] double[] BETA_X [22.3858,22.3858,22.3858,20.7061,19.0272,…] double[] ALPHA_X [8.91993,8.91993,8.91993,8.57440,8.21451,…] double[] ETA_X [0.00000,0.00000,0.00000,0.00000,0.00000,0.00000,…] double[] ETAP_X [0.00000,0.00000,0.00000,0.00000,0.00000,…] double[] PSI_Y [0.00000,0.00000,0.00000,0.0252115,0.0547781,0…] double[] BETA_Y [4.03080,4.03080,4.03080,3.59863,3.17969,…] double[] ALPHA_Y [2.32706,2.32706,2.32706,2.17425,2.01510,…]
double[] ETA_Y [0.00000,0.00000,0.00000,0.00000,0.00000,… ]
double[] ETAP_Y [0.00000,0.00000,0.00000,0.00000,0.00000,…]
getRdb (a trivial bash script), calls the rdbClient side
which calls rdbService (based on pvService).
rdbService's rdbServiceFactory looks up the SQL SELECT statement equivalent to the argument it was given in a table, and then executes that SELECT statement. It uses JDBC to get the data out of Oracle. The JDBC ResultSet is encoded as pvData and sent back to the client, and what you see is simply what you get on the client when you toString() the returned PVStructure.

## Slide 11: Too Early to Identify Version 4 Limitations
PVData does not preclude people from defining any arbitrary data strcuture.
PVAccess already supports the transportation of these non-normative types
We are not developing clients to support non-normative types.
Donald Rumsfeld --- “There’s your knowns, your known unknowns, and your unknown unknowns”……

## Slide 12: Create a V4 Archive Server
Distributed Front-Ends
?Refactor? XAL, MMLT, SDDS, GDA
Physical Device
Ethernet
Thin HLA Client
CAC
CAC
Control System Studio
CAC
Diag Database
CAS
Physical Device
PS Database
CAS
Physical Device
RF Database
CAS
Physical Device
Vac Database
CAS
Physical Device
Util Database
CAS
Matlab, SDDS, Python
CAC
Diamond Simulation
Diag & PS
CAS
Channel Archiver View
PVManager
PVAS
Channel Finder Server
SQL
RDB
PVAC
PVAC
PVAS
PVAS
PVAS
PVAS
PVAS
PVAS
PVAS
Unit Conversion
CAC
PVAC
PVAS
Orbit
CAC
PVAS
Alignment, Magnet Map..
SQL
IRMIS
PVAC
Multichannel Array
PVAS
PVAC
PVAS
Archive Retrieval
XML/RPC
Channel
Archiver
PVAC

## Slide 13: Conclusions
  The interface is intended to allow us to create a standard client/server architecture for high level applications such as: areaDetector, Matlab Middle Layer Toolkit, SAD, SDDS, XAL, GDA, MDS+
  NSLSII is committed to apply this technology to physics applications, and is actively evaluating it for application in experiment control and data acquisition.
  Low level applications are not yet being developed in Java IOC.
  New structures are easy to create – but we plan to carefully limit these to general and useful normative types.
  We are in the stage of development most similar to the transition from GTACS to EPICS: early, immature, risky, changeable, challenging, and fun.